## Slide 1: Communication System IICT Lecture 10

## Slide 2: What is Communication?
Computer communications describes a process in which two or more computers/devices transfer data, instructions, and information.
Some communications involve cables and wires; others are sent wirelessly through the air.
Figure shows a sample communications system.
Notes:   Act of transferring information from one place to another

## Slide 3
Communications systems contain all types of computers and computing devices. For successful communications, you need:
  Sending device: initiates an instruction to transmit data, instructions, or information.
  Communication device: connects the sending device to a communications channel.
  Communication channel: or transmission media on which the data, instructions, or information travel.
  Communication device that connects the communications channel to a receiving device.
  Receiving device that accepts the transmission of data, instructions, or information.

## Slide 4: Network Complexities

## Slide 5: What is a Protocol?

## Slide 6: Protocols in Daily Life

## Slide 7: Communication Protocol
A communication protocol is a system of rules that allows two or more entities of a communications system to transmit information via any kind of variation of a physical quantity.
  The protocol defines the rules, syntax, semantics and synchronization of communication and possible error recovery methods.
Hence, a protocol is a set of rules which governs the transfer of data between computers.
  Protocols allow communication between computers and networks.

## Slide 8: Characteristics of Communication System
There must be a Sender and Receiver
Handshaking is used to establish which protocols to use. Handshaking controls the flow of data between computers
Protocols will determine the speed of transmission, error checking method, size of bytes, and whether synchronous or asynchronous.

## Slide 9: Five Basic Components
Every communication system has 5 basic requirements
Data Source (where the data originates)
Transmitter (device used to transmit data)
Transmission Medium (cables or non cable)
Receiver (device used to receive data)
Destination (where the data will be placed)

## Slide 10: Pictorial Representation

## Slide 11: Network Model

## Slide 12: OSI Model
The Open Systems Interconnection model (OSI model) is a conceptual model that characterizes and standardizes the communication functions of a telecommunication or computing system without regard to its underlying internal structure and technology.
The OSI model also provides much more information which is included with each package.

## Slide 13: 7 Layers of OSI Model
OSI “Open System Interconnection”
OSI is not a protocol but a list of protocols divided between 7 layers with each layer having a different set of functions.
Each packet is layered/packaged with protocols from each of the layers as it is processed.
The process of layering the protocols around each package is called encapsulation. The final encapsulated data packet is called a frame.

## Slide 14: Layers of OSI Model
Some Mnemonics

## Slide 16: OSI Model

## Slide 17: OSI Model
OSI Reference Model

## Slide 18
Sender
Receiver

## Slide 19: Physical Layer

## Slide 20
Functions of Physical Layer:

## Slide 21: Data Link Layer
Functions of Data Link Layer:
The Network Interface Card (NIC) that you plug your Ethernet wire into handles the Layer 2 functionality.
It receives signals from the wire, and transmits signals on to the wire.
  Your Wi-Fi NIC works the same way, receiving and transmitting
  radio waves which are then interpreted as a series of 1’s and
  0’s.

## Slide 22
MAC (Medium Access Control)

## Slide 24
This Layer will group together those 1’s and 0’s into chunks known as Frames.

## Slide 25: Network Layer
The Network layer of the OSI model is responsible for packet delivery from end to end.
It does this by using another addressing scheme that can logically identify every node connected to the Internet. This addressing scheme is known as the Internet Protocol address, or the IP Address.
  It is considered logical because an IP address is not a permanent identification of a computer unlike the MAC address

## Slide 26
Functions of Network Layer:
Routers are Network Devices that operate at Layer 3 of the OSI model. A Router’s primary responsibility is to facilitate communication between Networks. As such, a Router creates a boundary between two networks. In order to communicate with any device not directly in your network, a router must be used.

## Slide 27: OSI Model – Layer 2 vs. Layer 3
When a computer has data to send, it encapsulates it in a IP header which will include information like the Source and Destination IP addresses of the two “ends” of the communication.
The IP Header and Data are then further encapsulated in a MAC address header, which will include information like the Source and Destination MAC address of the current “hop” in the path towards the final destination.
The interaction and distinction between Layer 2 and Layer 3 is crucial to understanding how data flows between two computers.
For example, if we already have a unique L2 addressing scheme on every NIC (like MAC addresses), why do we need yet another addressing scheme at L3 (like IP addresses)? Or vice versa?
The answer is: Both addressing schemes accomplish different functions:
Layer 2 uses MAC addresses & is responsible for packet delivery from hop to hop.
Layer 3 uses IP addresses & is responsible for packet delivery from end to end.
Notice between each Router, the MAC address header is stripped and regenerated to get it to the next hop. The IP header generated by the first computer is only stripped off by the final computer, hence the IP header handled the “end to end” delivery, and each of the four different MAC headers involved in this animation handled the “hop to hop” delivery.

## Slide 28: Transport Layer
The Transport layer of the OSI model is responsible for distinguishing network streams.
This Layer is responsible for service to service delivery
Specifically, two methods of distinguishing network streams exist. They are known as the Transmission Control Protocol (TCP), or the User Datagram Protocol (UDP).
Both TCP and UDP have 65,536 port numbers (each), and a unique application stream is identified by both a Source and Destination port (in combination with their Source and Destination IP address).
Example:
At any given time, a user’s computer have opened an Internet browser, while music is being streamed, while a messenger or chat app is running.
Each of these applications are sending and receiving data from the Internet, and all that data is arriving in the form of 1’s and 0’s on to that computer’s NIC.
Something has to exist in order to distinguish which 1’s and 0’s belong to the messenger or the browser or the streaming music. That “something” is Layer 4

## Slide 29: Transport Layer
Functions of Transport Layer:
Responsible for source- to-destination delivery of the entire message

## Slide 30
Layer 4 accomplishes task by using an addressing scheme known as Port Numbers.

## Slide 31: Session Layer
It defines how to start, control and end conversations (called sessions) between applications
Functions of Session Layer:
Session closure

## Slide 32: Presentation Layer
It defines the format in which the data is to be exchanged b/w two communication entities
Functions of Presentation Layer:

## Slide 33: Application Layer
It interacts with application programs and is highest level of OSI Model. It contains management functions to support distributed applications.

## Slide 34: Summary of Function of Layers
(Placing signals on the carrier)
(Error control and synchronization)
(Routing of data through network)
(Ensures error-free transfer)
(Set-up coordinate conversation)
(Format conversion)
(Identification, authentication)

## Slide 36: Service Performed at Each Layer
E-mail, Web browser, Directory
POP, SMTP, FTP, HTTP, DNS
Sockets
TCP
IP
PPP, Ethernet, Token ring
100baseT
Notes: I will not send data anymore until i get an acknowledgment.
this process is slow
It is used for security purpose
example: web, sending mail, receiving mail etc
UDP
Here i have no headache with acknowledgment.
this process is faster but here data can be lost .
example : video streaming , online games etc
TCP + UDP = SMTP(example : mobile,telephone)

## Slide 38: Transmitting and Receiving in Comm. Systems

## Slide 39: Serial Transmission
Data is transmitted, on a single channel, one bit at a time one after another
Much faster than parallel because of way bits processed (e.g. USB and SATA drives)

## Slide 40: Parallel Transmission
Each bit has it’s own piece of wire along which it travels
Often used to send data to a printer

## Slide 41: Why not to use Parallel instead Serial?
Due to inconsistencies on channels data arrives at different times
Because of the way it is transmitted packet switching cannot be used
The above two points makes parallel slower than serial and requires higher bandwidth.
Parallel transmissions are rarely used anymore

## Slide 42: Synchronous VS Asynchronous Transmission
Synchronous Transmission
All data sent at once and no packet switching
Asynchronous Transmission
Uses stop/ start bits
most common type of serial data transfer
Allows packet switching
Allows sharing of bandwidth (i.e. talk on phone while another person is using internet)

## Slide 43: Transmission Directions
Simplex:
One direction only

## Slide 44
Half duplex:
Both directions but only one direction at a time

## Slide 45
Full duplex:
Send and receive both directions at once.

## Slide 46: Network Topologies
Mesh Topology
Ring Topology
Bus Topology
Star Topology

## Slide 47: Mesh Topology

## Slide 48: Ring Topology

## Slide 49: Bus Topology

## Slide 50: Star Topology

## Slide 51: Network Hardware

## Slide 52: Bridge
Large networks can be separated into two or more smaller networks using a bridge. This is done to increase speed and efficiency. This type of network is called a segmented LAN and has largely been superseded by the use of switches which can transfer data straight to a computer and thus avoid bottleneck jams which bridges were designed to fix.

## Slide 53: Gateway
Often used to connect a LAN with a WAN.
Gateways join two or More different networks together.

## Slide 54: Some more
Routers: A router is a networking device that forwards data packets between computer networks. Can be used in place of a switch or bridge.
Switches: smart hubs which transmit packets to the destination port only
Hubs: like double adapters /power boards in the home except instead of plugging in extension cords we are plugging in computers to allow them to communicate.

## Slide 55: Transmission Media
Twisted pair – Ethernet cable
Coaxial cable –Thick black cable used for higher bandwidth communications than twisted pair (i.e. Optus cable)
Fiber optic – data transferred through pulses of light. Extremely fast.
Non cable methods such as satellite, microwave, wireless and Bluetooth

## Slide 56: End of the Lecture