## Slide 1: Flip-Flops
Reference: Chapter 5
Sequential Circuits
Moris Mano 4th Ediditon

## Slide 2: Revision

## Slide 3: Types of Logic Circuits
Combinational Logic Circuits
Sequential Circuits

## Slide 4: Combinational VS Sequential Circuits
Combinational Logic Circuits
  In which variables are combined by the logical operations
  Output depends on inputs and logic operations
Logic Diagram of a Combinational Circuit

## Slide 5: Combinational VS Sequential Circuits (contd.)
Sequential Circuits
  Which include storage elements
  Output depends on input and the value of storage element
Logic Diagram of a Sequential Circuit

## Slide 6: Storage Element
  Storage elements are circuits
    that stores binary information for indefinite time
    Can change their state(value stored) on the basis of input signal
Notes: We need 1-bit or n-bit storage elements

## Slide 7: Latches

## Slide 8: SR Latch
Input |  | Output |  | State
S | R | Q | Q’ | 
1 | 0 | 1 | 0 | Set
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 1 | Reset
0 | 0 | 0 | 1 | 
1 | 1 | 0 | 0 | Undefined
Timing diagram / Logic Simulation of SR Latch
Function Table
Graphic Symbol
Logic Diagram
Q
Q’

## Slide 9: S’R’ Latch
Input |  | Output |  | State
S’ | R’ | Q | Q’ | 
0 | 1 | 1 | 0 | Set
1 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | Reset
1 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | Undefined
Graphic Symbol
Function Table
Logic Diagram
Q
Q’

## Slide 10: SR Latch with Control Input
Input |  |  | 
C | S | R | Next State Of Q
0 | X | X | No Change
1 | 0 | 0 | No Change
1 | 0 | 1 | Q=0, Reset
1 | 1 | 0 | Q=1, Set
1 | 1 | 1 | Undefined
Function Table
Logic Diagram

## Slide 11: D Latch
C | D | Next State of Q
0 | X | No Change
1 | 0 | Q=0, Reset State
1 | 1 | Q = 1, Set State
Function Table
Logic Diagram
Timing Diagram of D Latch

## Slide 12: Synchronization in Digital Systems
Timing Device – Clock Generator
  Generates clock pulses
  Positive Pulse Negative Pulse
  Positive Edge Negative Edge

## Slide 13: Synchronization in Digital Systems
  Clock as control input of Latches
  Problem with Latches
  Transparency
  Solution  Flip-Flops
Notes: If control input = 1, 1000 changes in input signals result in 1000 changes at output of latch. This is what makes the latches transparent.

## Slide 14: Flip-Flop

## Slide 15: Types of Flip-Flops
Pulse-Triggered Flip-Flops
Edge-Triggered Flip-Flops

## Slide 16: Pulse-Triggered Flip-Flop

## Slide 17: SR Master Slave Flip-Flop
Graphic Symbol
Right angle means
Output signal
Changes at the end
Of the pulse
Pulse Triggered SR Master-slave Flip Flop
Accepts input signals at
Positive Pulse
Updates the output at
Negative Pulse
Q
Q’

## Slide 18: SR Master-Slave Flip-Flop
M
S
Characteristic Table
Logic Simulation of SR Master-Slave Flip-Flop

## Slide 19: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
Graphic Symbol
Q
Q’
Notes: Modified version of SR Flip-Flop
Eliminates undesirable condition (1,1)  Undefined State

## Slide 20: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
0
1
1
1
1
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
Notes: At time t, Flip-flop had value 0 saved in it. Now signal (1,1) is coming at time t+1.

## Slide 21: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
0
1
1
1
1
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
0

## Slide 22: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
0
1
1
1
1
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
1
0
0

## Slide 23: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
0
1
1
1
1
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
1
0
0
1
0
Which means save 1

## Slide 24: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
0
1
1
1
1
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
1
0
0
1
0
1
0

## Slide 25: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
1
0
Input Signal = (1,1)
Case 1:
Previous State = (0,1)
1
0
1
1
0
1
0
1
0

## Slide 26: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
0
1
1
1
Input Signal = (1,1)
Case 2:
Previous State = (1,0)
Notes: At time t, Flip-flop had value 1 saved in it. Now signal (1,1) is coming at time t+1.

## Slide 27: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
0
1
1
1
0
Input Signal = (1,1)
Case 2:
Previous State = (1,0)

## Slide 28: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
0
1
1
1
0
1
0
Input Signal = (1,1)
Case 2:
Previous State = (1,0)

## Slide 29: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
0
1
1
1
0
1
0
0
1
Input Signal = (1,1)
Case 2:
Previous State = (1,0)
Which means save 0

## Slide 30: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
0
1
1
1
0
1
0
0
1
0
1
Input Signal = (1,1)
Case 2:
Previous State = (1,0)

## Slide 31: Master-Slave JK Flip-Flop
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
Characteristic Table
1
1
0
0
1
1
0
1
0
1
0
1
Input Signal = (1,1)
Case 2:
Previous State = (1,0)

## Slide 32: Test Your Concepts
Can you fix the undefined state problem in SR and S’R’ latches?

## Slide 33: Pulse-Triggered Flip-Flop vs Edge-Triggered Flip-Flop

## Slide 34: Positive-Edge-Triggered D Flip-Flop
D | Q(t+1) | Operation
0 | 0 | Reset
1 | 1 | Set
Graphic Symbol
Characteristic Table
Triggers on
Positive Edge
of Control signal
Q
Q’

## Slide 35: Positive-Edge-Triggered D Flip-Flop
D | Q(t+1) | Operation
0 | 0 | Reset
1 | 1 | Set
Graphic Symbol
Dynamic
Indicator
Symbol
Characteristic Table
Q
Q’

## Slide 36: Negative-Edge-Triggered D Flip-Flop
Graphic Symbol
Triggers on Negative Edge of Control signal

## Slide 37: Positive-Edge-Triggered JK Flip-Flop

## Slide 38: Equations of Flip-Flops

## Slide 39: Equation of D Flip-Flop
D
D
Q(t+1) = D(t)

## Slide 40: SR Latch with Control Input
Logic Diagram

## Slide 41: SR Latch with Control Input
Logic Diagram
C = 1

## Slide 42: SR Latch with Control Input
Logic Diagram
C = 1
S’
R’

## Slide 43: SR Latch with Control Input
Logic Diagram
C = 1
S’
R’
(R’ Q(t) )’

## Slide 44: SR Latch with Control Input
Logic Diagram
C = 1
S’
R’
(R’ Q(t) )’
(S’ (R’ Q(t) )’ )’

## Slide 45: Equation of SR Flip-Flop
Q(t+1) = S(t) + R’(t)Q(t)
Q(t+1) is a function of input signals S and R at time t and Q(t)

## Slide 46: Equation of Positive-Edge-Triggered JK Flip-Flop
Q(t+1) = J(t)Q’(t) + K’(t)Q(t)