## Slide 1: Registers
Reference
Chapter 7
Moris Mano 4th Edition

## Slide 2: Positive-Edge-Triggered D Flip-Flop
D | Q(t+1) | Operation
0 | 0 | Reset
1 | 1 | Set
Graphic Symbol
Characteristic Table
Clock

## Slide 3: D Flip-Flop with Direct Inputs
Independent
Of clock
Clock
Notes: ( S , R ) = (0,1)  Bubbles at S and R inputs  ( 1 , 0 ) coming in the flip-flop  save 1 asynchronously
Reference: Page 221 Moris Mano 4th Edition

## Slide 4: 4-bit Register with parallel load
Logic Diagram
Symbol
Q3 | Q2 | Q1 | Q0
Register Contents:
Notes: Page 337 Moris Mano 4th Edition

## Slide 5: 4-bit Register with parallel load
Logic Diagram
Symbol
4 Flip-Flops
connected with
one clock
Reset functionality
for Register
(initialization)
to set all 4 bits
to zero (irrespective
of clock signal) i.e.
0 | 0 | 0 | 0
Q3 | Q2 | Q1 | Q0

## Slide 6: How 4-bit Register works?
Clock
What if we connect
Clock to first two
Flip-flops and
(Clock)’ to last
Two flip-flops?

## Slide 7: Register Load
Register Load:
“Transfer of new information into a register”
Parallel Loading:
All the bits of register loaded simultaneously with a common clock pulse

## Slide 8: Register Load
Problem:
Keep the data saved until user wants to change it i.e. Do not update contents with clock.
Solution:
Update register functionality such that:
Load = 0  Content unchanged even with clock
Load = 1  Follow the clock to change the contents

## Slide 9: Register Load
Methods to control Register Load:
Load control with Clock Gating
  Clock Gating: Prevent clock from reaching the flip-flops
Load control with D Input

## Slide 10: 1. Load Control with Clock Gating
C Input

## Slide 11: 1. Load Control with Clock Gating
Cinput = Load ’ + Clock
Load = 1:
Cinput = 0 + Clock
Cinput = Clock (X + 0 = X)
- Register is clocked normally
- New information is transferred into the register on positive edge of clock

## Slide 12: 1. Load Control with Clock Gating
Cinput = Load ’ + Clock
Load = 0:
Cinput = 1 + Clock
Cinput = 1
- Clock has been stopped to enter Flip-Flop
- No positive transitions on C Inputs, contents of registers remain unchanged

## Slide 13: 1. Load Control with Clock Gating
C Input
Clock stopped
Behind the gate
Clock being passed
To register

## Slide 14: 2. Load Control with D Input
Clock

## Slide 15: 2. Load Control with D Input
Clock
Enable

## Slide 16: 2. Load Control with D Input

## Slide 17: 2. Load Control with D Input
0
0
1
0
X . 0 = 0
X . 1 = X
Q
Q
Requirement: Enable = 0  Flip Flop Disabled  Retain Q

## Slide 18: 2. Load Control with D Input
1
1
0
D
X . 0 = 0
X . 1 = X
0
D
Requirement: Enable = 1  Flip Flop Enabled  Save Data D