## Slide 1: Registers
Reference
Chapter 7
Moris Mano 4th Edition

## Slide 2: Types of Registers
Registers with Parallel Load
  Simultaneously loading all bits from external input
Shift Registers
  Register which can shift its stored bits in one or both directions
  One bit (external input) being saved at a time

## Slide 3: 4-bit Register with parallel load
Logic Diagram
Symbol
Q3 | Q2 | Q1 | Q0
Register Contents:
Notes: Page 337 Moris Mano 4th Edition

## Slide 4: 1. Load Control with Clock Gating
C Input
Clock stopped
Behind the gate
Clock being passed
To register
Notes: Page 337 Moris Mano 4th Edition

## Slide 5: 2. Load Control with D Input
Clock
Notes: Page 339 Moris Mano 4th Edition

## Slide 6: What is this block doing?
Clock

## Slide 7: Shift Register
Clock
Symbol
External Input
Notes: Page 353 Moris Mano 4th Edition

## Slide 8: How Shift Register works?
Clock
Given:
Serial Input = 0 (constant)
Initial Value of Register = 1010
What will be the value of register after T1, T2, T3 and T4?
1
0
1
0
0
Positive Edge Triggered D Flip-Flop: Q(t+1) = D(t)

## Slide 9: How Shift Register works?
Clock
Given:
Serial Input = 0 (constant)
Initial Value of Register = 1010
What will be the value of register after T1, T2, T3 and T4?
0
1
0
1
0

## Slide 10: How Shift Register works?
Clock
Given:
Serial Input = 0 (constant)
Initial Value of Register = 1010
What will be the value of register after T1, T2, T3 and T4?
0
0
1
0
0

## Slide 11: How Shift Register works?
Clock
Given:
Serial Input = 0 (constant)
Initial Value of Register = 1010
What will be the value of register after T1, T2, T3 and T4?
0
0
0
1
0

## Slide 12: How Shift Register works?
Clock
Given:
Serial Input = 0 (constant)
Initial Value of Register = 1010
What will be the value of register after T1, T2, T3 and T4?
0
0
0
0
0

## Slide 13: Homework
Can you design a register which shifts the data left?

## Slide 14: Parallel vs Serial Mode
Digital System is said to operate in “Parallel Mode” when all the bits are transferred or manipulated at a time.
Digital System is said to operate in “Serial Mode” when information in the system is transferred or manipulated one bit at a time.

## Slide 15: What is this block doing?
Clock

## Slide 16: Serial Transfer
Clock
Notes: Page 375 Moris Mano 4th Edition

## Slide 17: How Serial Transfer Works?
Clock
Given:
Initial Value of Register A = 1011
Initial Value of Register B = 0010
What will be the value of both registers after T1, T2, T3 and T4?

## Slide 18: How Serial Transfer Works?
Clock
After T4:
B = A
A = 0

## Slide 19: Homework
What if after T4 we want:
  B = A and A = A
  Or
  B = A and A = B
  Or
  B = A and C = B and A = C

## Slide 20: Serial Transfer with Shift Control
Requirement:
If Shift = 1  Transfer Contents of registers
If Shift = 0  Retain data
How will you implement this functionality?

## Slide 21: Serial Transfer with Shift Control
Notes: Page 375 Moris Mano 4th Edition

## Slide 22: What is this block doing?
A3A2A1A0
B3B2B1B0
Notes: One pair of significant bits (Ai, Bi) is being added at one clock pulse. Page 377 Moris Mano 4th Edition

## Slide 23: Serial Addition
Why are we saving carry in flip-flop?
A3A2A1A0
B3B2B1B0
Si
C(i+1)
Notes: Page 377 Moris Mano 4th Edition

## Slide 24: Homework
How can you perform following functionality using the Serial Addition Circuit (without changing the circuit)?
A = A + B + C + D

## Slide 25: Shift Register with Parallel Load
Requirements:
Design a register which
  Behaves like a shift register, if Shift = 1
  Behaves like register with parallel load, if Load = 1
  Retains data, if Shift = 0 and Load = 0
Notes: Page 354 Moris Mano 4th Edition

## Slide 26: Shift Register with Parallel Load
Requirements:
Design a register which
  Behaves like a shift register, if Shift = 1
  Behaves like register with parallel load, if Load = 1
  Retains data, if Shift = 0 and Load = 0
Shift | Load | Operation
0 | 0 | No Change(Hold)
0 | 1 | Load Parallel Data
1 | X | Shift down from Q0 to Q3
Notes: Page 354 Moris Mano 4th Edition

## Slide 27: Shift Register with Parallel Load

## Slide 28
1
0
0
0
0
0
0
0
0
0
1
When Shift = 1
Shifting data right
Enabled
Enabled
Enabled
Enabled

## Slide 29
1
0
0
0
0
0
0
0
0
0
1
0
Load = 1 & Shift = 0
Parallel Load Data
Enabled
Enabled
Enabled
Enabled

## Slide 30
0
0
0
0
0
0
0
0
0
0
Load = 0 & Shift = 0
Retain previous data
Enabled
Enabled
Enabled
Enabled

## Slide 31
What is this circuit
Doing when
Load = 1 & Shift = 1
???

## Slide 32: Design a register with following requirements
Function Table
(Or Shift Left)
(Or Shift Right)
Q3 | Q2 | Q1 | Q0
Notes: Function table of Bidirectional shift register with Parallel Load

## Slide 33: What is this Circuit doing?
Notes: This is Bidirectional Shift Register with parallel Load. Page 355 Moris Mano 4th Edition

## Slide 34: What is this Circuit doing?
0
0
Qi(t+1) = Qi(t)
Retain Previous Data

## Slide 35: What is this Circuit doing?
0
1
Shift Left (or Shift Down)

## Slide 36: What is this Circuit doing?
1
0
Shift Right (or Shift Up)

## Slide 37: What is this Circuit doing?
1
1
Parallel Load

## Slide 38: Bidirectional shift register with Parallel Load

## Slide 39: Bidirectional shift register with Parallel Load
Make flip-flop level full circuit of 4-bit Bidirectional Shift Register with Parallel Load

## Slide 40: What will be the Serial Output for Bidirectional Shift Register?

## Slide 41: What will be the Serial Output for Bidirectional Shift Register?
Serial Out For Shift Left

## Slide 42: What will be the Serial Output for Bidirectional Shift Register?
Serial Out For Shift Right

## Slide 43: Serial In – Parallel Out Register
Design yourself